## Slide 1: Project Meeting
IoT Group
2019.05.10

## Slide 2: Performance of Raspberry pi execution
Data payload: 93 bytes * 200
  Per data: 88 bytes
  Payload size: 1+2+88+2 bytes
Buffer size: at least 18600 bytes

## Slide 3: Data size and Character length
Data content:
  Smart meter data ID
  Time stamp
  Energy
Data type: string
  English
  Number
  Symbol
Data size:
  English: 1byte
  Number: 1byte
  Symbol: 1byte
  Space: 1byte

## Slide 4: Python Socket Multiple Clients
Progress work : Multi-Connection Client
Future work : Send data to a specific client

## Slide 5: Flow Chart of Working Architecture
LoRa
Antenna
(SX1276)
LoRa Sensor node ( Raspberry Pi 3 )
Smart meter
Simulator.py
LoRa
Antenna
(SX1276)
LoRa Gateway ( Raspberry Pi 3 )
Smart meter Dataset.csv
LoRa transmission.py
LoRa receipt.py
DNN
container
BC
container
Message
Management program
LoRaWAN
Packet Forwarding program
WiFi, Ethernet
Cloud

## Slide 6: Packet Forwarding program
Progress work:
  Study and modify code from LoRa® to suitable our gateway
The code description:
  a program running on the host of a Lora gateway that forwards RF packets receive by the concentrator to a server through a IP/UDP link
Source: https://github.com/Lora-net/packet_forwarder
Notes: There is no authentication of the gateway or the server, and the acknowledges
are only used for network quality assessment, not to correct UDP datagrams
losses (no retries).

## Slide 7: Sequence diagram
Gateway
Server
When LoRa packets are received
Data (token X, GW MAC, JSON payload)
ACK (token X)
Process packets
Notes: PUSH_DATA
That packet type is used by the gateway mainly to forward the RF packets
received, and associated metadata, to the server.
網關使用該分組類型主要用於轉發RF分組收到的和關聯的元數據到服務器
PUSH_ACK
That packet type is used by the server to acknowledge immediately all the
PUSH_DATA packets received.
服務器使用該數據包類型立即確認所有數據包收到PUSH_DATA數據包。
0 | protocol version = 2
1-2 | random token
3 | PUSH_DATA identifier 0x00
4-11 | Gateway unique identifier (MAC address)
12-end | JSON object, starting with {, ending with }, see section 4

## Slide 8: Thanks!

## Slide 9: Raspberry Pi 3 B Baseline
Pi State | Power Consumption
Idle | 350 mA (1.9W)
ab –n 100 –c 10 (uncached) | 950 mA (5.0W)
400% CPU load (stress –cpu 4) | 980 mA (5.1W)